| Technical Data Sheet – DS025098E |  | VISLINK Marine & Energy |
| --- | --- | --- |
| Cable Coax RG59 Mini IEC 332.1 HERNIS Cables |  |  |
| Order Info |  |  |
| HERNIS Part No: | 025098 |  |
| Coax |  |  |
| Impedance at 5MHz: Attenuation: Capacity: Conductor: Dielectric: Diameter centre Leader & Dielectric: Screen: Recommended Cable Length:: | 75( ( 3( Max. 3.3dB/100m 55pF/m nominal 0.22mm2, 7 x 0.2mm bare Copper Cellular Polyethylene 2.44mm ( 0.13mm 0.127mm bare Copper braid, 85% nominal coverage Max.250m |  |
| Overall Characteristic |  |  |
| Cable Weight: Outer Diameter: Bend Radius: Sheath: Oxygen Index: HCL Emission: Operating Temperature Range: Mud Resistance: Flame Retardant: Colour/Marking: Standard Drum Length: | 33g/m 5.0mm ( 0.25mm Min. 50mm Orange, Halogen free, Flame retardant thermoplastic 40 Less than 0.05%, tested per BS 6425: Part 1 -30°C ~ +80°C Resistant to Petro Free Drilling Mud, NEK606 IEC 332/1 Orange, “HERNIS 25098” 500m (10% (Longer must be ordered specially) |  |
|  | Note: All data in the data sheet are subject to change without any further notice. |  |
| HERNIS Scan Systems A VISLINK Marine & Energy Company | Head office: Arendal, Norway Subsidiary, Houston: Tel: +47 37 06 37 00 Tel: +1 281 560 8050 cctv@hernis.com cctv.houston@hernis.com Subsidiary, Singapore Subsidiary, Brazil: Tel: +65 65 45 9068 Tel: +55 22 2773 5465 cctv.singapore@hernis.com cctv.brasil@hernis.com |  |